## Slide 1
Performance Evaluation of an Off-road Light Aerial Platform for Date Palm Cultivation
Authors: Francesco Bonechi, Francesco Garbati Pegna and Enrico Bonaiuti
Department of Agricultural, Food and Forestry Systems (GESAAF), University of Florence, Florence, Italy.
E-mail: francesco.bonechi@stud.unifi.it

## Slide 2
Date Palm Cultivation
Date palm (Phoenix dactylifera L.) cultivation has grown extraordinarily in the last decades.
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
World Production Dates (t) | 6440583 | 6659971 | 6720722 | 6748537 | 6626357 | 6552820 | 6770193 | 6963171 | 7018737 | 7183101 | 7525890 | 7262843 | 7430261 | 7517294 | 7600312 | 8139037 | 8460443
World Area Harvested Dates (ha) | 1051482 | 1058342 | 1086165 | 1095182 | 1070818 | 1081629 | 1147494 | 1184448 | 1182885 | 1200803 | 1282856 | 1126732 | 1121587 | 1160096 | 1161048 | 1251998 | 1353159
 | 2000 | 2016
World Production Dates (t) | 6,440,583 | 8,460,443
World Area Harvested Dates (ha) | 1,051,482 | 1,353,159
FAOSTAT, 2018

## Slide 3
This positive trend is also forcing date cultivation to develop new solutions to face the modern production challenges:
Timeliness of agricultural practices;
Increasing labor costs;
Difficult and risky operations when palm height is over 6-8 m;
Scarcity of skilled labor.
Date Palm Cultivation

## Slide 4
In most plantations access to the frond level is still performed in traditional ways. This is mainly due to:
Date Palm Cultivation
High cost of mechanization;
Lack of specific machinery for date palm cultivation.

## Slide 5
A major change that has occurred in 1950s has been the mechanization of some cultivation practices in particular the timing and method of harvesting.
Nowadays some of the machines available for harvesting are:
Palm stem shakers:
Suitable for those varieties of dates where fruits do not ripen at the same time.
Date Palm Mechanization

## Slide 6
Date Palm Mechanization
Limits may be identified in:
High purchase price and maintenance costs;
Difficulties of maneuvering;
Heavy machines;
Operators have to jump out from the platform to reach the fruits if the bunches are hidden by the fronds.
Large “U” shaped aerial platform:
Widely used in large specialized plantations where valuable varieties are cultivated. Offers good levels of efficiency and safety for workers.

## Slide 7
The Aerial Platform
Aiming at addressing the mechanization problems of medium and small sized farms, two Italian companies ERREPPI and CO.ME.T. developed Xiraffe, an off-road light aerial platform, easily adaptable to diverse operating conditions.
This machine constitutes a novelty in this sector for its characteristics and its suitability to work in harsh conditions and could represent a rentable solution for field operations at frond level.

## Slide 8
The Aerial Platform
Xiraffe is a compact aerial platform, consisting of an articulated hydraulic boom lift mounted on a 4 wheel drive power unit.
The unit is 3.75 m long and 1.85 m wide with a total weight of 1,680 kg.
Easy to manoeuvre in all the type of soils , without damaging the irrigation systems and respecting the environment of the plantation.

## Slide 9
The vehicle
The power unit is a compact all-terrain tractor powered by a Yanmar 435 cc air cooled Diesel engine, with a maximum power output of 8.3 kW.
Transmission is part-time type, allowing to select traction of 2 or 4 wheels.
Average fuel consumption is about 0.7 l/h at an engine speed of 3,000 rpm.
It’s provided with a rear hitch for towing a 500 kg trailer.
The Aerial Platform

## Slide 10
The platform
The aerial part is composed by a basket held by an articulated boom lift, supported by four hydraulic outriggers.
The outriggers are suitable for uneven terrain and can be adjusted to a maximum difference in height of 0.78 m.
The Aerial Platform

## Slide 11
The platform
The basket is provided with a 230 V electric outlet and a compressed air outlet for connecting different tools such as secateurs, chainsaw, sprayers etc.
External canisters can be also hung on the basket’s railing to collect the harvested dates.
The Aerial Platform

## Slide 12
Maximum height: 9.8 m (basket floor);
Maximum outreach: 4.5 m;
Maximum loading capacity: 150 kg;
Turret rotation range: 360°;
The Aerial Platform
The basket can be raised to its full extension in 40 s;
The aerial system can be guided by two fully hydraulic controls.

## Slide 13
Evaluation Method
This study analyses the performances of Xiraffe focusing on the harvesting operations; the investigation is based on data collected in 2017, during field trials in Medjool plantations in Jordan Valley (H.K. of Jordan).
The evaluation was conducted by comparing manual and mechanically assisted harvesting in terms of time and productivity and recording fixed, variable and out-of-pocket costs.

## Slide 14
Study Area
The tests were carried out in three different farms located in:
Middle Jordan Valley, municipality of Ma’addi, Al-Balqa governorate.

## Slide 15
Study Area
The farms
Al-Sughaiyer Co. plantation, a 5.2 ha farm leased with a 5-year contract. 700 Medjool palms with 8 x 8 m plant spacing.
Jeneidi farm, a family-run grove of 3.7 ha with 455 Medjool palms with a 9 x 9 m plant spacing.
Arar farm owned by an entrepreneur with a 30 ha total area and 2,700 Medjool palms with an 8 x 8 m pattern.
Since most of the palms in the farms were less than 15 years old, it was difficult to find plants that were sufficiently tall to make trials significative.
Generally these palms were characterized by a high leaf density.

## Slide 16
Methodology
120 leaves
High density, clusters completely covered by the frond.
100 leaves
Medium density, clusters are still inside the frond but is much easier to reach them.
90 leaves
Low density, few clusters are out from the frond and all of them are easily reachable.

## Slide 17
Methodology
The time for carrying out the different operations in the manual and mechanically assisted harvesting was measured by the use of a chronometer. And these are:
Transfer

## Slide 18
Methodology
Placing

## Slide 19
Methodology
Lifting

## Slide 20
Methodology
Harvesting

## Slide 21
Methodology
Descending

## Slide 22
Methodology
Unloading

## Slide 23
Methodology
Disengaging

## Slide 24
Methodology
Servicing date palms with Xiraffe can be done in two different ways:
“360°”
“180°+180°”

## Slide 25
Manual Harvest
The traditional manual harvesting was done by skilled operators climbing up the palms, sometimes with the help of a ladder, and placing the collected fruits in a small bucket and lowering it to the ground with the use of a rope.

## Slide 26
Results
The easiness of access to the date clusters depends mainly on their position, being frond coverage and height from the ground the most important factors.
Chart: Height of clusters from the ground (m)
| 3 | 3.8 | 4.4000000000000004 | 4.5 | 4.5 | 5.4 | 6.3 | 6.4 | 7.4 | 7.5 | 7.6 | 8.4 | 8.6 | 9.3000000000000007 | 9.4 | 10
Accessible clusters | 80 | 63.1579 | 100 | 33.3333 | 100 | 100 | 100 | 100 | 100 | 100 | 75 | 100 | 100 | 100 | 100 | 90.9091
Leaves | 90 | 90 | 90 | 120 | 90 | 90 | 100 | 100 | 100 | 120 | 120 | 100 | 100 | 100 | 100 | 100
The machine proved to be fully efficient in reaching clusters in a range between 4.4 and 9.4 m height with a normal frond density of about 100 leaves per plant.

## Slide 27
Results
However, when cluster height is lower than 6 m, the boom geometry makes the platform progressively more difficult to manage because of the projection of the lower sections and the possibility of contact with the outriggers or other parts of the machine.

## Slide 28
Results
Chart: Trials
| Trial 1 | Trial 2 | Trial 3 | Trial 4 | Trial 5 | Trial 6 | Trial 7 | Trial 8
Harvesting time | 0.018044 | 0.013866 | 0.012824 | 0.018414 | 0.035463 | 0.026215 | 0.025127 | 0.029028
Amount harvested | 35 | 21 | 15 | 36 | 120 | 93 | 102 | 120
The average time for harvesting one palm was of 32’13” with two operators involved.
Harvesting time varied greatly from one palm to another being influenced by the different frond characteristics and amount of dates to be harvested. This is because when the total amount of dates per palm exceeds 60 kg, an intermediate unloading is necessary, increasing the total time of the session.

## Slide 29
Results
Chart: Time sharing between the different operations
| Transfer | Placing | Lifting | Intermediate Unloading | Harvesting | Unloading | Descending | Disengaging
 | 1.5214 | 5.5197 | 4.5825 | 13.1877 | 64.6482 | 3.3471 | 4.2296 | 1.3389
Unloading of dates should be better organized since this was the slowest operation besides harvesting taking 13.19% of the total time.
In particular, the canisters didn’t turn out to be a satisfying solution and should be redesigned.

## Slide 30
Results
Chart: Different harvesting techniques
| 360° 180°+180° Manual
"360°" | 126.1769
"180°+180°" | 92.3696
Manual | 133.6877
The results show that, in terms of productivity, the “360°” technique proved to be the most effective for the harvesting within the optimum height range.
In this type of environment, manual harvest demonstrated to be faster than using Xiraffe. This was true when harvest sessions were short. Longer is the harvest and lower is the advantage of manual harvest.

## Slide 31
Results
Chart: Average of time needed for each operation (min:s)
| Placing | Lifting | Harvest+Unload | Descending | Disengaging
Xiraffe "360°" | 0.0016117 | 0.0014308 | 0.017425 | 0.0012384 | 0.00031973
Manual | 0.00034722 | 0.0013932 | 0.019413 | 0.00031829 | 0
Machine harvesting is slower than manual harvesting in the placing, descending and disengaging phases, but it’s faster in the harvesting and unloading operations even if the tests were in a manual harvesting friendly environment because of the high density of the fronds and the general low height of the plants.

## Slide 32
Results
Method | Manual |  | Xiraffe “360°” | 
Height(m) | 8 | 7.6 | 8.4 | 7.5
Quantity (kg) | 35 | 90 | 36 | 96
Time (h:mm:ss) | 0:20:30 | 1:01:37 | 0:26:31 | 0:40:24
Total (kg/min) | 1.71 | 1.48 | 1.36 | 2.38
Time for harvesting largely depends on the amount to be collected.
When palms were above 7 m and more than 60 kg of dates had to be harvested Xiraffe proved to be much more efficient.

## Slide 33
Support in the harvest of dangerous palms

## Slide 34
Availability of additional pneumatic tools

## Slide 35
Reduction of workers' efforts allowing employment in other activities

## Slide 36
Low impact on the farm environment
Fuel consumption was in the range of 0.75 l/h

## Slide 37
Conclusions
Xiraffe is able to reach and easily work in areas where access for larger machines would be too invasive;
Ensure access to the frond level in a safe and easy way;
The advantages observed during harvesting can be envisaged also in all other aerial operations, though their specifics will make them more or less pronounced;
As normal when mechanization is introduced in agriculture, also the crop should be adapted to the machines, making their action easier.

## Slide 38
Conclusions
The capacity of better performing where palms are taller and bear high yield makes the use of Xiraffe a possible option for well-established and tended plantations. Even if the economic analysis has not yet been completed, it is possible to foresee that this kind of mechanization is accessible to larger farms or by pooling, or for contractors which can better exploit this kind of equipment.

## Slide 39
Basket capacity;
Unloading the harvested dates without descending.
It is possible to foresee the opening a new scenario in commercial date palm cultivation, though further tests should be carried out, after reviewing some of its’ characteristics, possibly on larger scale.
This study, that was the subject of a MSc thesis, is worth being extended, due to the potentialities of the machine of becoming a benchmark in date palm cultivation, even through a specific PhD in cooperation with manufacturers, date producers and research and education institutions which are the main stakeholders involved in this subject.
Possible Improvements

## Slide 40
Thanks for your attention!