## Slide 1
Application of soil erosion models in the Gumara-Maksegnit watershed
Andreas Klik, Hailu Kendie, Nigus Melaku, Roman Schiffer, Stefan Strohmeier, Chris Renschler, Omotayo Akinjiyan, and Claudio Zucca
Institute of Hydraulics and Rural Water Management
University of Natural Resources and Life Sciences, Vienna
Universität für Bodenkultur Wien
Department für Wasser-Atmosphäre-
Umwelt
Final Project Meeting
Bahir Dar,
June 20-21, 2016

## Slide 2
Why do we use simulation models?
Advantage of soil erosion modeling (Bork, 1991)
Efficient and fast assessment of short-, mid- and long-term impacts of different land use and land management scenarios
Analysis and evaluation of interactions between processes
Identification of research gaps
Evaluation of climate change impacts on runoff and erosion
Model requirements
Applicable to the problem
consistent and repeatable results
cover full range of conditions (climate, soils, vegetation, management,....)
can be used with available resources
quality of results adequate and comparable
transferability to other regions
SWAT Soil and Water Assessment Tool
WEPP Water Erosion Prediction Project
Partly physically based, partly stochastic
Large river basins (several 1000 km²)
Continuous simulation
Physically based
Small catchments (> 10 km²)
Continuous and single storm simulation
Applied soil erosion models

## Slide 3
SWAT model input
Landuse
Soil texture classes
Digital elevation model
Derived from satellite images
Five soil texture classes based on field sampling
Climate data 1997 - 2013
Two crop rotation were implemented in the model: sorghum – chickpea - teff
sorghum - faba bean - barley

## Slide 4
Chart: Rainfall 2012
| 41094 | 41095 | 41096 | 41097 | 41098 | 41099 | 41100 | 41101 | 41102 | 41103 | 41104 | 41105 | 41106 | 41107 | 41108 | 41109 | 41110 | 41111 | 41112 | 41113 | 41114 | 41115 | 41116 | 41117 | 41118 | 41119 | 41120 | 41121 | 41122 | 41123 | 41124 | 41125 | 41126 | 41127 | 41128 | 41129 | 41130 | 41131 | 41132 | 41133
Rain | 4.8 | 17 | 11.4 | 38.8 | 30.8 | 14 | 2.2 | 19 | 9.8 | 0 | 4.4 | 1.4 | 11.8 | 9.8 | 18 | 21.8 | 16.4 | 12.2 | 3.8 | 17 | 30.2 | 14.4 | 2 | 32.2 | 21.6 | 0.8 | 1.8 | 1.2 | 10.8 | 32 | 14.2 | 6.6 | 23.2 | 2.8 | 8 | 13.2 | 10 | 7 | 9.6 | 15.4
Chart: Observed runoff, Aba-Kaloye & Ayaye 2012
| 41094 | 41095 | 41096 | 41097 | 41098 | 41099 | 41100 | 41101 | 41102 | 41103 | 41104 | 41105 | 41106 | 41107 | 41108 | 41109 | 41110 | 41111 | 41112 | 41113 | 41114 | 41115 | 41116 | 41117 | 41118 | 41119 | 41120 | 41121 | 41122 | 41123 | 41124 | 41125 | 41126 | 41127 | 41128 | 41129 | 41130 | 41131 | 41132 | 41133
Aba-Kaloye (untreated) | 0.18431 | 2.6782 | 4.1208 | 1.0162 | 2.3387 | 0.2671 | 0.50113 | 0.994 | 3.2703 | 3.1523 | 1.9463 | 6.2897 | 1.2617 | 5.7324 | 2.6866 | 3.0792 | 2.7343
Ayaye (treated) | 1.0155 | 2.2408 | 0.72806 | 1.4704 | 0.70657 | 1.3349 | 2.7055 | 2.0786 | 1.2732 | 2.4765 | 3.5938 | 1.524 | 4.721 | 1.5823 | 1.4225 | 0.93011 | 0.35702 | 0.8845 | 2.2964
SWAT calibration data
Chart: Observed sediment yield Aba-Kaloye & Ayaye 2012
| 41094 | 41095 | 41096 | 41097 | 41098 | 41099 | 41100 | 41101 | 41102 | 41103 | 41104 | 41105 | 41106 | 41107 | 41108 | 41109 | 41110 | 41111 | 41112 | 41113 | 41114 | 41115 | 41116 | 41117 | 41118 | 41119 | 41120 | 41121 | 41122 | 41123 | 41124 | 41125 | 41126 | 41127 | 41128 | 41129 | 41130 | 41131 | 41132 | 41133
Aba-Kaloye (untreated) | 1.81 | 2.26 | 27.11 | 129.31 | 13.6 | 45.36 | 1.78 | 3.47 | 7.09 | 69.76 | 31.86 | 15.81 | 55.37 | 16.94 | 18.01
Ayaye (treated) | 0.07 | 22.47 | 60.62 | 10.01 | 23.29 | 10.95 | 14.97 | 24.62 | 30.86 | 23.47 | 54.75 | 7.2 | 9.88 | 1.94

## Slide 5
Results
Influence of the soil conservation measures in Ayaye
Ayaye (treated WS) delivers 42% less runoff and 47% less sediment yield than Aba Kaloye

## Slide 6
Results
Calibration results Aba-Kaloye – calibration period 2012
Observed and estimated runoff Aba-Kaloye 2012
Observed and estimated runoff Ayaye 2012

## Slide 7
Results
Calibration results Aba-Kaloye – calibration period 2012
Observed and estimated sediment yield Aba-Kaloye 2012
Observed and estimated sediment yield Ayaye 2012

## Slide 8
 | Precip mm | Untreated t/ha | Treated t/ha
2006 | 1482 | 30.9 | 19.1
2007 | 1480 | 29.7 | 13.3
2008 | 1206 | 32.8 | 24.5
2009 | 1041 | 34.6 | 27.5
2010 | 1119 | 40.3 | 30.8
2011 | 1397 | 77.9 | 105.3
2012 | 942 | 18.4 | 6.5
Average |  | 37.8 | 32.4
Seasonal budget sediment yield Model period 2001-2012, warm up period 5 years
 | Teff | Sorghum | Barley | Wheat | Chickpea | Faba Beans
 | kg/ha | kg/ha | kg/ha | kg/ha | kg/ha | kg/ha
Goal | 1700 | 1200 | 2400 | 2500 | 2600 | 3000
Simulation | 1512 | 898 | 2248 | 2576 | 2398 | 2951
Mean crop yield – model period 2001-2012
-14%

## Slide 9
GeoWEPP - Watershed simulation
Representative processes
for hillslopes and channels
(aggregation before WEPP run)
Representative processes for distributed flowpaths
(aggregation after WEPP run)
On-site Assessment
Flowpath Method
Off-site Assessment
Watershed Method

## Slide 10
Off-site Assessment
Watershed Method
On-site Assessment
Flowpath Method
WEPP Watershed Model

## Slide 11
WEPP inputs – Land use Google Earth – October 2011
Land use map derived from Google Earth

## Slide 12
WEPP inputs – Stone bunds

## Slide 13
WEPP inputs
Crop and mnagement files from WEPP data base and adapted to Ethiopian conditions (e.g. crop height, crop coverage, crop density, max. crop yield, tillage depth, surface roughness,…)

## Slide 14
WEPP results - On Site Spatial soil erosion and deposition pattern within the watershed
1 T = 10 t / ha / yr
Period 2012-2014

## Slide 15
71 storms produced 808.53 mm.
Aba Kaloye (without stone bunds)
43 events produced 146.7 mm of runoff
Total contributing area to outlet = 31.80 ha
Avg. Ann. total hillslope soil loss = 3284 tonnes/yr
Avg. Ann. total channel soil loss = 623 tonnes/yr
Avg. Ann. sediment discharge from outlet = 2230.3 tonnes/yr
Avg. Ann. Sed. delivery per unit area of watershed = 70.1 T/ha/yr
Sediment Delivery Ratio for Watershed = 0.571
Ayaye (with stone bunds)
40 events produced 150.2 mm of runoff
Total contributing area to outlet = 25.83 ha
Avg. Ann. total hillslope soil loss = 2337 tonnes/yr
Avg. Ann. total channel soil loss = 334 tonnes/yr
Avg. Ann. sediment discharge from outlet = 1253 tonnes/yr
Avg. Ann. Sed. delivery per unit area of watershed = 48.5 T/ha/yr
Sediment Delivery Ratio for Watershed = 0.469
No change in runoff but 31% less sediment yield in Aba Kaloye than in Ayaye
Gumara Maksegnit Watershed, Ethiopia

## Slide 16
Ayaye with stone bunds
40 events produced 150.2 mm.of runoff
Total contributing area to outlet = 25.83 ha
Avg. Ann. total hillslope soil loss = 2337 tonnes/yr
Avg. Ann. total channel soil loss = 334 tonnes/yr
Avg. Ann. sediment discharge from outlet = 1253 tonnes/yr
Avg. Ann. Sed. delivery per unit area of watershed = 48.5 T/ha/yr
Ayaye without Stonebunds
40 events produced 148.8 mm. of runoff
Total contributing area to outlet = 24.08 ha
Avg. Ann. total hillslope soil loss = 1728 tonnes/yr
Avg. Ann. total channel soil loss = 425 tonnes/yr
Avg. Ann. sediment discharge from outlet = 1345 tonnes/yr
Avg. Ann. Sed. delivery per unit area of watershed = 55.9 T/ha/yr
Appr. 14% reduction in sediment yield due to stone bunds
Comparison – Ayaye with and without stone bunds

## Slide 17
Surface runoff average runoff coefficient increases from 0.11 to 0.12
Sediment yield average sediment yield increases by 32% (2030), 96% (2060) and 168% (2090)
Max sediment yield increases by 84, 195, and 332%
Crop yield
No impact on faba bean but significant decrease for wheat and barley
Impact of Climate Change
WEPP hillslope model
50 m length
9% slope no stone bunds considered
Climate Scenarios for Bahir Dar: 2015, 2030, 2060, 2090 (100 yrs simulation)
Climate scenarios with minimum, average and maximum precipitation

## Slide 18
Summary and Conclusions
General conclusions
Data need for distributed physically based models higher than for stochastic models
Type of model dictated by the availability of data (USLE vs. process-based)
Performance of models on a longer term basis mostly good to acceptable
Runoff prediction usually better than soil loss assessments
Most soil erosion models are developed in humid regions; crop, management and SWC parameterization need to be adapted to regional specific conditions
Quality of output depends on quality of input data and the ability of the model to represent the driving processes
Never perform simulations from your desk without knowing exactly the watershed!
WEPP
- Higher input data need (climate, crop, management,…)
+ Better understanding and representation of processes
+ Derivation of model parameters which can be implemented into large scale lumped models
SWAT
Sub-daily processes are not reflected (high intensity rainfall!)
- Capability on sub-catchment scale remains open question
+ Lower input data requirement and therefore applicable to large basins
+ Transparent calibration procedure available (uncertainty!)